## Slide 1: Nvidia GPU Scheduling Analysis
Group Member 13: Yiming Li, Ximing Chen
Estimated Total Hours: 50

## Slide 2: Plans (Past Week)
Explore the GPU block-to-SM distribution policy.

## Slide 3: Testing Framework
Kernel Generation: Create and dispatch random kernel sequences to GPU until full.
Execution: Sequential execution of kernels; thread blocks assigned to specific SMs.
Prediction and Analysis: Predict SM assignments using a round-robin algorithm; analyze differences.
Iterative Refinement: Refine prediction algorithm based on discrepancies to match actual GPGPU behavior.

## Slide 4: Testing Kernel
Kernel Functionality:
  Gathers and logs block and thread IDs, SMIDs.
  Simulates workloads using registers and shared memory.
  Implements controlled execution delays.
Register Usage Control:
  Employs `-maxrregcount` to limit and specify register usage.
  65,536 registers per SM
Register Control’s Impact on Local Memory:
  Inverse relationship between register and local memory usage.
  Configures to minimize execution hindrance due to memory reconfiguration.

## Slide 5: Plans (Next Week)
Conduct experiments on this testing framework and analyze the result.